## Slide 1: Apollo Command and Service Module (CSM)
Team A9: Hunter Donn, Ethan MacDonald, Eric Oh, Gracelyn Pham, Jack Saunders

## Slide 2: The Apollo Program
17 missions throughout 1961-1972
  6 crewed missions
Third US human spaceflight program carried out by NASA
Designed to safely land humans on the Moon and bring them back

## Slide 3: Mission Profile
Liftoff
Saturn V S-1C powered flight
S-1C/S-II separation
Launch escape tower jettison
S-II/S-IVB separation
Earth parking orbit
Translunar injection
Command Service Module (CSM) separation from Launch Module (LM) adapter
CSM docking with LM/S-IVB
CSM/LM separation from S-IVB
Midcourse correction
Lunar orbit insertion
Pilot transfer to LM
CSM/LM separation
LM descent
Touchdown
Explore surface, set up experiments
Liftoff

## Slide 4: Spacecraft Data
Command Module
  Mass: 5,560 kg
  Crew: 3
  Length: 3.5 m
  Diameter: 3.9 m
Service Module
  Mass: 24,520 kg
  Crew: N/A
  Length: 7.6 m
  Diameter: 3.9 m
First launch: February 26, 1966
Last launch: July 15, 1975

## Slide 5: Command Module Baseball Card Summary
Design Constraints/Parameters
Pressurized volume: 10.4 m3
Habitable volume: 5.9 m3
RCS: 12 410 N thrusters
RCS propellants: MMH/N2O4
RCS propellant mass: 120 kg
Structure: truncated cone
Electric system batteries: 3 40 Ah silver-zinc batteries; two 0.75 Ah
silver-zinc pyrotechnic batteries
Drinking water capacity: 15 kg
Waste water capacity: 26 kg
CO2 scrubber: lithium hydroxide
Odor absorber: activated charcoal
Parachutes: 2 4.9 m conical ribbon drogue parachutes; 3 2.2 m ringshot pilot parachutes; 3 25.5 m ringsail main parachutes
Description: The CM was a conical structure that housed the 3 men crew of the Apollo missions and carried equipment for atmospheric reentry and splashdown. It was made of an aluminum honeycomb sandwich bonded between sheet aluminum alloy. The base of the CM consisted of a heat shield made of brazed stainless steel honeycomb filled with a phenolic epoxy resin. The CM was divided into three compartments: forward, aft, and crew and had five windows: one in the access hatch, one next to each astronaut in the two outer seats, and two forward-facing rendezvous windows. The CM provided the re-entry capability at the end of the mission after separation from the SM.

## Slide 6: Service Module Baseball Card Summary
Design Constraints/Parameters
RCS thrust: 440 N
RCS propellants: MMH/N2O4
SPS engine thrust: 91,000 N
SPS engine propellants: (UDMH/N2H4)/N2O4
SPS Isp = 314 sec
𝛥V = 2,800 m/s
Electrical system: 3 1.4 kW 30 V DC fuel cells
The SM was a cylindrical structure attached to the back of the CM. The outer skin of the SM was formed by thick aluminum honeycomb panels while the interior was divided by milled aluminum radial beams into six sections around a central cylinder. The back of the SM had a gimbal mounted restartable hypergolic liquid propellant engine and cone shaped engine nozzle. At the top were electrical power system radiators and spaced around the bottom were environmental control radiator panels.

## Slide 8: CSM Beauty Shots

## Slide 9: Capsule with Launch Vehicle Beauty Shot

## Slide 10: Command Module Interior
Couches
Storage
Control Panels
Pressure Hull

## Slide 11: Command Module Interior

## Slide 12: Service Module Interior
Bird’s Eye Sector View
Detailed View

## Slide 13: Service Module Interior

## Slide 14: Exterior by Person with Launch Vehicle
Purple: Eric
Yellow: Ethan
Red: Hunter

## Slide 15: Exterior by Person
Purple: Eric
Yellow: Ethan
Red: Hunter

## Slide 16: Service Module Interior by Person
Orange:Jack

## Slide 17: Command Module Interior By Person
Yellow: Ethan
Purple: Eric
Blue: Gracelyn